## Slide 1
Advanced VMRS Coding for Maintenance Labor Alerting with a Connected Ecosystem

## Slide 2: Purpose & Scope:
To develop a Code Key and/or Instruction Set of maintenance Labor alerts to be used as a common language that will indicate when maintenance labor is required to be performed!
These alerts can be used across all vehicle original equipment manufacturers (OEMs), engine manufacturers and component suppliers.
Preventive Parts Replacements: Through multiple meetings and excellent collaboration we have found an approach that only requires ONE additional code key for Maintenance Items Only!

## Slide 3: Objective:
To create a common language / schema in TMC’s Vehicle Maintenance Reporting Standards (VMRS) that can be leveraged by vehicle OEMs, engine manufacturers and component suppliers to digitally communicate Maintenance Labor Alerts with feedback of accomplishment. This will require a new code key for maintenance items to be established.
Note: This is task force is focusing on the VMRS Codes Only!
  Other elements like parts and labor that may be structured in the API offering will be addressed by the technology providers.

## Slide 4: Current Participants:
Jack Poster | VMRS God! (TMC)
Matt Farcosky | S5 Fleet Maintenance Mgmt. Chair (Fleet Pro)
Brian Mulshine | Task Force Group Chair (Navistar)
Partners: OEM’s, Engine Companies, Software Providers & Customers

## Slide 5: Discussions: Better Together!
We recently had a meeting with TMC and a few OEM’s that had some idea’s on how this can be designed in a better support a wider audience.
Preventive Parts Replacement: M-Z codes, we as a team are recommending, we do not combine in the “New Maintenance Labor Code Key”
  Rationale: Preventive Parts Replacement Items in most cases are a Part to replace and should leverage code key 33!
Maintenance Labor Alerts: We all agreed to move forward with a recommendation to request the addition of a new code key for “Maintenance Labor Alerts”. This new code key will still be identified by starting at letter “A” and can go all the way to “Z” but we do not ever expect to need all letters.
Status Codes: Other Feedback
Preventive Parts Replacement: We determined that the Preventive Repairs are about Parts and best represented in Code Key 52 Parts Status Codes.
Maintenance Labor Alerts: These items are more about Labor and should be identified in Code Key 16 “Maintenance Labor Alerts”
The following slides will explain this in more detail.

## Slide 6: Preventive Parts Replacement:
Code Key 33
Part Identification
Code Key 52
“Part Status Code”
Which its primary purpose is to identify the status of a part. Our recommendation is to leverage CK 52 for Preventive Parts Replacement

## Slide 7: Example: Maintenance Alerts - Remaining Useful Life
Remaining Useful Life / aka: RUL
Multiple vehicle and engine manufacturers have data currently or becoming available soon:
  Oil Condition / Life
  Oil Filter
  Fuel Filter
  Air Filter
  DEF Filter
  DPF Filter
  Transmission Oil & Filter
Technology can improve TCO by providing “Insights” for accurate Dynamic Data Driven Intervals!
This will take time to evolve – Need to start the foundation elements now!

## Slide 8: Requirements / Needs:
Truck / Manufacturer / Dealers
FMS / Customer
Service Requirements – Due Soon, Past Due, Replace Soon
Service Requirements – Due Soon or Past Due
Past Due
  Oil Change, Fuel Filter, Lube Driveline
Due Soon
  Valve Lash Adjustment, DEF Filter
Past Due
  Lift gate, Oil Change, Fuel Filter, Lube Driveline
Performed
  Air Dryer, Valve Lash Adjustment, DEF Filter
Service Event – AT Dealer (Service Provider) “Pull Request”
Telematics Data
OEM Data

## Slide 9: Requirements / Needs:
Truck / Manufacturer / Dealers
FMS / Customer
Service Requirements – Performed (Items, Date, Odometer / Engine Hours)
Dealer Maintenance Performed ( Provider, RO #, Items, Date, Odometer / Engine Hours)
Need to Update Systems – Both Sides

## Slide 10: What is the Desired Outcome:
Customer / Fleet
Fleet Mgmt. Systems
  Vehicle Manufacturers
  Engine Manufacturers
  Transmission Manufacturers
  Fleet Management Systems
  Service Providers
  Vehicles / Trailers
  Telematics Providers
Data Generators

## Slide 11: Maintenance Alert Elements:

## Slide 12: VMRS Coding for Predictive Alerts:
New VMRS Code | VMRS ALL Maintenance Desc. | International | Freightliner | Detroit
 | Engine Oil and Oil Filter Change? | Lube Oil & Filter Change |  | Engine Oil and Filter Change
 | Etc. | Fuel Filter Replace | Fuel Filter Replacement | Fuel Filter Change
 |  | Valve Lash Adjustment |  | Adjustment Valve Lash
 |  | Engine Belts and Belt Tensioner - Inspect | Inspect Accessory Drive Belts | Belts and Tensioner Inspection
 |  | Release Bearing / Shafts / Fork – Lubricate | Clutch Release Bearing Lubrication* | 
 |  | Aftertreatment Diesel Exhaust Fluid Dosing Unit Filter - Change |  | DEF Pump Filter Change

## Slide 13: Discussion – Potential Path:
“Proposed” New Maintenance Labor Alerts Codes: Starting with Letters to protect prior art:
  We will start with the letter “A” and leverage sequential characters when required!

## Slide 14: Status Codes: For Maintenance Alerting
Code Key 16 “Repair Priority Class”
Code Key 16 is indicating when a labor function needs attention. Our recommendation is to leverage CK 16 for Maintenance Labor Alerts and add the 3 bottom items!

## Slide 15: Example: Maintenance Alerting
Below are the data element structure for creating a VMRS full description request:
System Group - 31
Code Key 16
Maintenance Alert Codes - XX
Code Key 31 – Available
No Change Required!
Code Key 16 – Available
Add New Statuses Needed!
Proposed New Code
“044” : Engine Fuel System
“04” : Due Soon
“A03” : Fuel Filter Replacement
“043” : Engine, Exhaust System
“05” : Past Due
“A04” : DPF Cleaning
Predictive Maintenance Example:
“044” : Engine Fuel System
“06” : Performed
“A03” : Fuel Filter Replacement
“043” : Engine, Exhaust System
“06” : Performed
“A04” : DPF Cleaning
After Service is Performed:

## Slide 16: API Potential Payload:
Duration to Past Due
  Mi. or Km.
  Engine Hours
  Days
Parts Required VMRS Codes
API Payload
API Payload:
044-A03-012 (Fuel Filter Replacement – Due Soon)
  Due At Miles: 152,001
  Due At Kilometers: 244,621
  Engine Hours:
  Days:
  Special Message:
Required Parts: 044-002-002, Qty. 1, Each (Gallons, Quarts, Liters, Pint – etc.)
(Element - Fuel Filter, Primary)

## Slide 17: API Potential Payload:
Parts API End Point:
VIN + 044-002-002 to Get Part Numbers & Descriptions!

## Slide 18: API Potential Payload:
API Payload:
GET: VIN Maintenance Data
POST: VIN Maintenance Data (For Updates)
GET: Parts Details (Send VIN + Part(s) VMRS)
GET: Service Information (Send VIN + Op(s) VMRS)

## Slide 19: RP 802F: Update required for RP 802F to “G” (T)

## Slide 20: RP 802F: Example Paragraph for Document
One Example: Component Level Codes “Code Key 33”
In order to provide a common generic term for each part within a vehicle, the system and assembly codes are further subdivided to the component level. This is accomplished through the use of an additional three-digit part identifier code. These codes should not be confused with the manufacturers 'or suppliers' unique identification(part) numbers, but rather should be considered universal identifiers or generic terms for the part. For example, a front brake lining can be identified by the following combination of System/As­sembly/Component codes-013-001-015.
A complete listing of Code Key 33 appears else where in the VMRS Implementation Handbook.
This code key should be leverage when implementing Predictive Repair strategies!

## Slide 21: RP 802F: Proposed Added Paragraph for RP
Maintenance Labor Alerts “Code Key XX”
Code Key XX enables the creation of standardizing the Maintenance & Inspections Alert requirements. This will also enable the ability to be digitally communicated between integrated vehicle manufacturers and component suppliers, fleet management systems and service providers in a common identification format. This key can be leveraged to improve accuracy of work accomplishment by identifying each desired maintenance item that is required by event.
Below is an example of a required Engine Oil Change that also requires the fuel filter to be replaced soon:
Note: Refer to RP 545 provides support for implementation of key performance indicators (KPI’s) that fleet management can use to track the performance of its vehicle operations.
Maintenance Definition: Preventive maintenance is the act of performing regularly scheduled maintenance activities to help prevent unexpected failures in the future. – Examples include but not limited to Oil Change Service at 75K Miles, Transmission Fluid Flush and Change at 300K Miles, Adding Coolant at a regular service, Valve Lash Adjustment at 500K Miles.
Code XX | Description | Code Key 16 | Description
045-A02 | Engine Oil and Filter - Replacement | 04 | Due Soon
044-A03 | Fuel Filter (Engine Mounted) - Replacement | 05 | Past Due

## Slide 22: RP 802F: Advantages to VMRS
There are 15 distinct advantages to using VMRS:
VMRS improves Preventive Maintenance:
Update to: VMRS Improves Preventive Maintenance Programs:
Add Language:
This code set provides the standardization for maintenance labor alerts into a common language.
Codes can be utilized for data integrations between systems such as OEM’s, Fleet Management Platforms and Service Providers.

## Slide 23: Next Steps:
Please Communicate:
Need your feedback at your earliest opportunity.
We need to provide the Recommended Draft to TMC Connect by August 8th
Next Meeting:
TMC Fall Conference – Cleveland, OH.
  Sept. 17th – 21st
  https://tmcfall.trucking.org/

## Slide 24: Questions / Discussion? Thank You!