## Slide 1
Advanced VMRS Coding for Predictive and Prognostic Maintenance
Exploratory Group

## Slide 2: Current Participants: Need Ecosystem Agreement!
TMC | Fleets | OEM’s | Engine Manufacturers | Technology Providers

## Slide 3: Task Force Name - Discussion:
Advanced VMRS Coding Predictive and Prognostic Maintenance

## Slide 4: Definitions:
Predictive Maintenance (PdM): is a type of condition-based maintenance that monitors the condition of assets through sensor devices. These sensor devices supply data in real-time, which is then used to predict when the asset will require maintenance.
Prognostic Maintenance (also known as condition-based maintenance, predictive maintenance, or simply prognostics) is the ability to know the condition of equipment, and to plan and perform maintenance accordingly before a critical failure.

## Slide 5: Purpose & Scope:
To develop Code Key(s) and/or Instruction Set(s) of predictive / prognostic maintenance items to be used as a common language to indicate required/needed service. (And Performed)
These items can be used across all vehicle original equipment manufacturers (OEMs), engine manufacturers and component suppliers.

## Slide 6: Objective:
To create a common language / schema in VMRS (ATA Codes) to be leveraged by vehicle OEMs, engine manufacturers and component suppliers to digitally communicate “predictive” Maintenance & Repair requirements.
  Predictive Maintenance: Components or Systems identified to have scheduled maintenance requirements expected to be performed.
      Examples Include: System Filters, Lubricants, Inspections, Adjustments and Cleaning
  Predictive Repair: Components that are identified to require servicing to prevent an unexpected usage interruption.
      Examples Include: Batteries, Sensor’s and Valve’s, Calibration Updates that do not have a PM Schedule.
Note: This is covering task force is focusing on the VMRS Codes Only!
    Other elements like parts and labor will be structured in the API offering by the data provider.

## Slide 7: Example: Predictive Maintenance

## Slide 8: Example: Predictive Maintenance - RUL
RUL: Remaining Useful Life
Multiple vehicle and engine manufacturers have data currently or becoming available soon:
  DPF Filter
  Air Filter
  Oil Filter
  Oil Condition / Life
  Fuel Filter
  ….

## Slide 9: Predictive Repair Example:
Attachment:
Current Use Case: Example!
Since “No Standard is Available” fleets receive and email data attachments.
Customers are expected to take data and enter into native system.

## Slide 10: Requirements / Needs:
Truck / Manufacturer / Dealers
FMS / Customer
Service Requirements – Due Soon, Past Due, Replace Soon
Service Requirements – Due Soon or Past Due
Past Due
  Oil Change, Fuel Filter, Lube Driveline
Due Soon
  Valve Lash Adjustment, DEF Filter
Past Due
  Lift gate, Oil Change, Fuel Filter, Lube Driveline
Performed
  Air Dryer, Valve Lash Adjustment, DEF Filter
Service Event – AT Dealer (Service Provider) “Pull Request”
Telematics Data
OEM Data

## Slide 11: Requirements / Needs:
Truck / Manufacturer / Dealers
FMS / Customer
Service Requirements – Performed (Items, Date, Odometer / Engine Hours)
Dealer Maintenance Performed ( Provider, RO #, Items, Date, Odometer / Engine Hours)
Need to Update Systems – Both Sides

## Slide 12: What is the Desired Outcome:
Customer / Fleet
Fleet Mgmt. Systems
  Vehicles / Trailers
  Service Providers
  Truck Manufacturers
  Engine Manufacturers
  Transmission Manufacturers
  Telematics Providers
  Trailer Manufacturers
  Eco Systems Partners
Data Generators

## Slide 13: Maintenance Elements:

## Slide 14: VMRS Coding for Predictive:
New? VMRS Code | VMRS ALL Maintenance Desc. | International | Freightliner | Detroit
 | Engine Oil and Oil Filter Change? | Lube Oil & Filter Change |  | Engine Oil and Filter Change
 | Etc. | Fuel Filter Replace | Fuel Filter Replacement | Fuel Filter Change
 |  | Valve Lash Adjustment |  | Valve Lash Adjustment
 |  | Engine Belts and Belt Tensioner - Inspect |  | 
 |  |  | Engine Drive Belt Inspecting | 
 |  | Release Bearing / Shafts / Fork – Lubricate | Clutch Release Bearing Lubrication* | 
 |  | Aftertreatment Diesel Exhaust Fluid Dosing Unit Filter - Change |  | DEF Pump Filter Change
Team Agreement!

## Slide 15: Discussion – Data Needs:
Below are the data element structure for creating a VMRS full description request:
System Group
Part Status
Predictive Maint. & Repair Codes
Code Key 31 – Available
No Change Required!
Code Key 52 – Available
Add New Statuses Needed!
Possible New Code
“044” : Engine Fuel System
“012” : Due Soon
“A03” : Fuel Filter Replacement
“043” : Engine, Exhaust System
“013” : Past Due
“A04” : DPF Cleaning
Predictive Maintenance Example:
“032” : Cranking System
“015” : Inspection and Replace if Failed - Soon
“M01” : Predictive Repair for Battery(s)
Predictive Repair Example:

## Slide 16: Discussion – Potential Path:
“Proposed” New Predicative & Prognostic Maintenance Codes: Starting with Letters to protect prior art:
  “A” through “L” – Reserved for Predictive Maintenance Codes
  “M” through “Z” – Reserved for Predictive Repair Codes

## Slide 17: Discussion – Status:
Status / Disposition:
Code Key 52 identifies the status of an equipment subsystem, assembly, or part. Its primary usages are for comparative maintenance analysis purposes and for inventory control purpose
Proposed to leverage the Parts Status Code Key 52.
Requested to propose the required elements for Predictive & Repair disposition.
Our proposed “Highlighted” are open for discussion…
Explanation & Discussion!

## Slide 18: Discussion & Needs:
Concerns:
  Governance of the requests
Other Allied Partner OEM’s:
  Body Manufacturer’s (Morgan, Supreme, etc.)
  Trailer Manufacturers
  Transmission Providers
  Refrigeration (Carrier or TK)
  Lift Gates
  Dolly’s
  Allied Equipment Providers

## Slide 19: Next Meeting:
Please Subscribe to TMC Connect! Only 6 Following!
Next Meeting - TMC in Orlando!
  Feb. 27th – Monday S-5 Meeting